## Slide 1: Predicting Machine Failure from Process Parameters
AI IN MANUFACTURING · COURSE PROJECT
Failure prediction, explanation and safe operating ranges on the AI4I 2020 predictive-maintenance dataset
GROUP 11
Muhammed Muhyudheen
B250355ME
Mohammed Hisham Kavumpurath
B251001ME
Athira T B
B250718ME
Aradhana SK
B250689ME
Notes: Speaker 1 (~20s) Good morning, sir, and everyone. We are Group 11. I'm [your name], and with me are [names]. Our project is called “Predicting Machine Failure from Process Parameters”. In simple words: can a machine's own readings warn us before it breaks down?

## Slide 2: Why predict machine failure?
An unplanned breakdown stops the line, scraps parts and forces urgent repairs. If a machine's own settings reveal rising risk, the team can act before it fails.
Our three goals
1
Predict the probability that a run will fail
2
Explain which settings drive that risk
3
Recommend safe operating ranges per product type
How it helps in a real plant
Maintenance before breakdown
Flag high-risk runs so inspections happen before a failure, not after it.
Smarter tool changes
Risk rises about 40× once tool wear passes ~200 min, so tools can be changed on schedule.
Safe operating windows
Keep power and torque inside the band where the model and the physics agree risk is low.
Notes: Speaker 1 (~120s) Imagine a factory machine that suddenly breaks in the middle of a shift. The production line stops, the parts it was making are wasted, and the repair has to happen in a hurry. That is expensive. But a machine gives us clues all the time: how fast it spins, how much twisting force it uses, how hot it runs, and how worn its cutting tool is. Our idea was to use these clues to spot danger early. This idea is called predictive maintenance: fixing a machine just before it fails, instead of after it breaks, or on a fixed schedule that may be far too early. We set three goals. First, predict: for every run of the machine, estimate the chance that it will fail. Second, explain: show which settings push that risk up. Third, recommend: give safe settings for each product type, so the operator knows how to run the machine safely. [point right] This is why it matters in a real plant. One, maintenance can happen before a breakdown, not after it. Two, smarter tool changes: we found the risk jumps about forty times once a tool has been used for around two hundred minutes, so tool changes can be planned. Three, safe operating windows: a range of power and force where the risk stays low. To do all this we needed data, and [Speaker 2] will now show you what our data looks like.

## Slide 3: AI4I 2020: 10,000 machining runs, only 3.4% fail
10,000
machining runs, no missing values
6
inputs: product type + 5 process readings
3.39%
of runs fail (339 failures)
28.5 : 1
healthy-to-failure ratio
Chart: Failure types (a run can have two)
| Heat dissipation | Overstrain | Power | Tool wear | Random
Runs | 115 | 98 | 95 | 46 | 19
Answer-giving columns removed
Five columns record which failure happened. They give the answer away (data leakage), so the model never sees them.
Rare failures handled
Always saying “no failure” is 96.6% accurate but useless, so we score how well failures are found (PR-AUC).
Notes: Speaker 2 (~70s) Thank you. We used a public dataset called AI4I 2020. It records ten thousand runs of a milling machine. For each run we know six things: the product's quality type, two temperatures, the speed, the torque, which is the twisting force, and how worn the tool is. And we know whether it failed. Here is the catch: only 339 runs failed. That is just 3.4 percent, about one failure for every 28 healthy runs. [point to chart] The chart shows the five types of failure. This creates two traps. [point to cards] First, five columns record which type of failure happened. They give the answer away, like reading the answer key during an exam, so we removed them. This mistake is called data leakage. Second, because failures are rare, a lazy model that always says “no failure” is 96.6 percent accurate, and still useless. So instead of accuracy, we use a score called PR-AUC, which measures how well the real failures are found.

## Slide 4: Workflow: from raw data to safe operating ranges
1
Check the data
Explore it, and remove the columns that give the answer away
2
Add physics features
Power, temperature gap, and wear × torque
3
Balance the data
Create extra failure examples (SMOTE), only from training data
4
Compare 3 models
Each tested 5 times on data it never saw (cross-validation)
5
Tune and set the alarm
Best settings found; alarm set to catch about 9 in 10 failures
6
Explain and recommend
Show why each prediction was made (SHAP), then find safe settings
Main score: PR-AUC, how well real failures are found · every result is averaged over 5 tests · fully repeatable
Notes: Speaker 2 (~70s) Here is how we built the solution, in six steps. One, we checked the data and removed the columns that give the answer away. Two, we added three features from physics: power, the temperature gap, and tool wear times torque, because these are what actually break machines. Three, failures are rare, so we created extra failure examples for the model to learn from, with a method called SMOTE, and only from the training data, never from the test data. Four, we compared three models. Each was tested five times on data it had never seen. This is called cross-validation, and it makes the results trustworthy. Five, we fine-tuned the best model and set its alarm so it catches about nine out of ten failures. Six, we explained its decisions and turned them into safe settings. [Speaker 3] will now show you the results.

## Slide 5: Results: Random Forest finds failures best (PR-AUC 0.915)
Chart: Precision–recall: the score we use
Chart: ROC: looks good for every model
89.4%
of failures caught
recall ± 1.6%
52.2%
of alarms are real
precision ± 3.6%
+0.040
better than XGBoost
won all 5 tests
Higher is better on both charts. Every prediction comes from a model that never saw that run. Random guessing would score 0.034. Alarm level 0.056, set to catch about 9 in 10 failures.
Notes: Speaker 3 (~70s) Thanks. The winner was the Random Forest, with a score of 0.915 out of 1. For comparison, random guessing would score only 0.034. [point to left chart] This chart shows the key trade-off. Moving right means catching more failures; staying high means fewer false alarms. The orange line, our Random Forest, stays at the top the longest, so it is the best. The score we use is simply the area under each line: the bigger, the better. The blue line, the simplest model, drops quickly, because machine failures don't follow straight-line rules. [point to middle chart] This second chart is a popular way to compare models, but notice that all three look good on it. That is exactly why we did not rely on it. [point to cards] In practice, our model catches 89 percent of failures before they happen, and about half of its alarms are real. The other half are cheap extra inspections, a fair price for catching nine out of ten breakdowns.

## Slide 6: Summary: accurate, explainable and physically sound
Reliable prediction
Score 0.915 out of 1 (guessing: 0.034); catches about 9 in 10 failures.
Physics features matter
Power, temperature gap and wear × torque raised the score by 0.08–0.14.
Honest evaluation
Always tested on unseen data. A careless setup would have faked 0.999.
Explains itself
Its explanations (SHAP) match the machine's real failure rules.
Recommended operating window
4.75 – 8 kW
power band to stay inside
< 200 min
tool wear: change the tool before this
≤ 54 Nm
max torque (58.5 Nm for Type M)
≥ 1,390 rpm
minimum speed when the temperature gap is below 8.6 K
Try it live:
ai4i-machine-failure-prediction.streamlit.app
Notes: Speaker 3 (~60s) To sum up, four points. Our predictions are reliable. Adding features from physics made a big difference. Our testing was honest: a careless setup could have shown a fake, near-perfect score of 0.999. And the model can explain itself: its reasons match the machine's real failure rules, even though we never told it those rules. [point right] For a factory, this becomes simple advice: keep power between 4.75 and 8 kilowatts, change the tool before 200 minutes of use, keep torque below 54 newton-metres, and when the temperature gap gets small, keep the speed above 1,390 rpm. We also built an interactive dashboard, where anyone can move these settings and instantly see the risk change.

## Slide 7: Thank you
Questions?
Live dashboard ai4i-machine-failure-prediction.streamlit.app
GROUP 11
Muhammed Muhyudheen · Mohammed Hisham Kavumpurath · Athira T B · Aradhana SK
Notes: Speaker 3 (~10s) Thank you for listening. We're happy to take your questions, and [console person] can show you the live dashboard.